|  | On-load Tap-changer Order Specifications | Guizhou Changzheng Electric Co.,Ltd. |
| --- | --- | --- |
| Purchaser |  |
| Contact |  | Tel |  | Fax |  | Mail |  |
| Order date |  | Delivery time |  | Quantity of OLTC |  |
| Transformer Data |
| Transformer model |  | Transformer user |  | Transformer produce No. |  |
| Application | Power Capacity regulation Furnace Rectifier Generator Others( ) | No.of Phases | 3-phase Single phase Others ( ) |
| Rated capacity | Constant( )kVA Variable( )kVA, decreasing from position( ) | Ambient temperature | -25~+40℃ -40~+40℃ Others( ) |
| Transformer type | Seperated winding transformer Auto-transformer Booster transformer | Frequency | 50Hz 60Hz |
| Overload | According to IEC 60354 ＞IEC60354 ( )% overload for ( )hours |
| Magnetic flux | Constant flux voltage regulation Variable flux voltage regulation（please attach transformer nameplate） Combined voltage regulation（please attach transformer nameplate） |
| Rated voltage and regulating range | ( )kV ( ) ×( )% － ( )×( ) % or ±( )×( )% |
| Configuration of tap winding （If special connection, please provide connection diagram and attach the transformer nameplate.） | (Y connection neutral (Y connection middle (Y connection terminal (Delta connection terminal point regulation) regulation) regulation) regulation) (Delta connection (1+2 phase regulation) (Auto terminal regulation) (Auto middle regulation) Middle regulation) |
| Transformer rated service current | I=( )A Transformer max. service current：Imax.=( ) A |
| Rated step voltage for each phase | Constant Ust=( )V Variable Ust max.= ( )V Ust min.= ( )V |
| Arrangement of coil A B Others (drawing is attached additionally) If the arrangement of coil is different from the illustrations, please attach the drawing. | Data： h= r1= r2= r3= r4= h1= a= b= |
| Potential resistance Yes (extra charge) No |  |
| Potential switch Yes (extra charge) No |  |
| On-load Tap-changer |
| Model | No.of phase | Max. rated through current (A) | Y / D | Equipment Max. ( voltage (kV) | Tap selector grade (not suitable for combined type switch) | Basic connection method |
|  |  |  |  |  | A B C D |  |
| Definition of operating positions | Max. effective turns on position: Middle position on position： Min. effective turns on position: Voltage regulating gear No.: |
| Mounting flange | Bell type Box type |
| Arrangement of head cover | With blasting cap (standard offer) | With pressure release valve, without blasting cap(extra charge) Electrical signal output wiring diagram follow technical data Standard, I type, II type |
| Arrangement of output shaft of head | Arrangement according to figure________from technical data. Note: If don’t designated this item, we will arrangement according to standard |
| Protective relay Standard offer Others（charge the price difference） | QJ4-25 a pair of normal open trip connection point, a pair of normal open signal connection point (standard offer) QJ4G-25, a pair of normal open trip connection point QJ4-25A (equips with gas box) a pair of normal open trip connection point, a pair of normal open signal connection point QJ6-25, two pair of normal open trip connection point |
| Length of horizontal drive shaft Unit：mm （extra charge for the over standard part） | H1=1000 (standard offer） H1 =( ) H2 =( ) H3 =( ) H4 =( ) Others（ ） Note：H1、H2、H3、H4 is the required drive shaft while multiple mechanical linkage (please check the technical data) (horizontal shaft equips with shielding case, if the length exceeds 2m, then the middle supporting box is necessary, please check the technical data) |
| Length of vertical drive shaft Unit: mm （extra charge for the over standard part） | V1=2000（standard offer） Others（ ） |
| Connection terminal shielding case | Combined type with shielding case, compound type without (standard offer) Compound type equips with shielding case (extra charge) |
| Insulation strength(kV) | Rated applied withstand voltage(50Hz1Min) | Rated impulse withstand voltage (1.2/50μs) |
| Tap-changer to the ground |  |  |
| Between the max. and min. tap of the same phase voltage regulation winding (a) |  |  |
| Between the contacts of the tap selector at selectable tap position (a1) |  |  |
| Between the selectable taps of the different phase voltage regulation winding (b) |  |  |
| Coarse regulation winding initial terminal of same phase and current lead out terminal of same phase(c1) |  |  |
| Between the contacts (c2）of different phase coarse regulation winding beginning terminal (-) |  |  |
| Between the beginning and end terminal (d) of the same phase coarse regulation winding |  |  |

| Motor drive mechanism data |
| --- |
| Model | MA7B（suitable for combined type tap-changer） MA9B（suitable for V type tap-changer） MAE（suitable for whole tap-changer） |
| Motor circuit | Standard offer：380V/50Hz 3AC/N Others( ) |
| Control and heating circuit | Standard offer：220V/50Hz AC Others( ) |
| Basic configuration |
| MA7B/MA9B | MAE |
| 1. A group of one to one tap position signal output; 2. Over-current blocking: input passive normal close connection point; 3. Remote control instruction input: passive empty connection point input; 4. A group remote control/local change-over switch position signal output; 5. Close and open signal output of protective circuit breaker; 6. A group of motor operating signal output; 7. A group of oil filter instructions signal output; 8. A group of remote position monitor connection cable socket; 9. Recording of operating times | 1. Two group of one to one tap position signal output: the inside of motor drive mechanism tank output one group, the other group is output from the controller; 2. Over-current blocking: input the passive normal open connection point; 3. Remote control instruction input: passive empty connection point input; 4. Condition signal output: high and low position limit, rising and drop, three operating mode (contact load capability: 1A/240V AC，0.5A/24V DC) 5. Oil filter signal output (contact load capability: 1A/240V AC，0.5A/24V DC); 6. Operating mode switching of local, motor drive mechanism and remote operation; 7. A group of BCD code tap position signal output (contact load capability: 1A/240V AC，0.5A/24V DC) 8. Tap position signal analog quantity DC1-5V voltage, 4-20mA current output; 9. RS485 communication: transfer the tap position and operating instruction according to 101 communication protocols; 10. Power source lacking phase, anti-phase measure blocking, lamplight alarming indication; 11. Device abnormal signal output: self inspect faults and power source faults signal output; 12. Recording of operating times。 |
| Basic scope and others (it is standard offer while no choosing) |
| MA7B/MA9B | MAE |
| Controller | CY40（standard offer） CY40A CY40B | CZK-100B（standard offer） YK-5（automatic regulating） |
| Cable length (extra charge if exceeds 30m) | 19 core( )m | 1 9 core and 5 core ( )m respectively (note: the max. is 250m) |
| Cable material | KVVR（polyvinyl chloride control cable (standard offer) KVVR22（polyvinyl chloride armour control cable） Others( ) |
| Hinge position of motor drive mechanism | Left (open the door to the left) (standard offer) Right (open the door to the right) | Nameplate | Chinese and English (standard offer) Other ( ) |
| Color of paint | Aircraft gray hammer paint (standard offer) Others( ) | Operating instructions | a set of Chinese（standard offer） Others( ) ( )set |
| Selectable configuration (extra charge) |
| Increase one to one tap position signal output | A group Two groups Three groups |
| Increase BCD code tap position signal output | A group Two groups |
| On-load tap-changer online oil clean device | Yes Not |
| Others | Mounting sealing gasket additionally Additional accessories Increasing temperature and humidity controller |
| Other requirements: |